## Slide 1: Pinnacle Points
Points from which no higher point can be seen
Jamie Breault
June 10, 2026

## Slide 2: About Me: Jamie Breault
Master of Data Science at UBC
6 years developing insurance software
Undergrad in Physics at the University of Waterloo
Avid backpacker
  52 multi-day hikes
  Often wonder if I am at the highest point in sight

## Slide 3: Data Sources
Global Summits
  25 million summits with over 100 feet of prominence
OTOTW Mountains
  6500 summits where no land rises above its horizontal plane
Open-Meteo’s Elevation API
  Fetches elevation by latitude and longitude
Beyond Horizons
  73 extreme lines-of-sight confirmed by photograph

## Slide 4: Finding Pinnacle Points
Every OTOTW mountain is a pinnacle point candidate. For each:
Validate higher local summits to test if line-of-sight analysis is worthwhile
Do line-of-sight analysis for summits that pass validation
  Earth’s curvature with topography
  Atmospheric refraction
  Atmospheric scattering
If no higher summits have line-of-sight with the candidate, then it is a pinnacle point

## Slide 5: Maximum Horizon Distance (MHD)
MHD is the maximum distance that can be seen from a point assuming all surroundings are at sea level
Line-of-sight is impossible if the distance between the observer and target is greater than the sum of their MHDs
MHD1
MHD2

## Slide 6: Earth’s Curvature with Topography
Space points 100 m apart between the observer and target
For each, get elevation and distance from observer
Transform to a physically representative coordinate system
Before Step 3:
After Step 3:

## Slide 7: Atmospheric Refraction
Determine the minimum light curvature needed for all confirmed lines-of-sight to be theoretically possible (k=6.4)
Use this curvature whenever doing line-of-sight analysis for pinnacle point candidates

## Slide 8: Atmospheric Scattering
A point’s scattering coefficient (β) can be calculated from its altitude (hL)
Integrate over the light’s path to get the average (βavg)
Calculate contrast (C), >0.02 is required for visibility

## Slide 9: Partial Irradiation
Extreme lines-of-sight are observed just before sunrise when there is partial irradiation to increase contrast.
Suppose there are two regions, the final region is fully irradiated and the first region is reduced by a factor α.

## Slide 10: Result and Validation
1553 pinnacle points were identified. An interactive map was shared online:
prominence@groups.io on Email
  Mountain metric specialists
  World-record-holding mountaineers
r/mountaineering on Reddit
  Mountaineering enthusiasts
The 4 confirmed errors discovered so far are the result of inaccuracies in elevation data.

## Slide 11: Next Steps
Investigate alternate light modelling solutions based on feedback

## Slide 12
Questions?